## Slide 1: Introduction to Verilog HDL
Mainak Chaudhuri
Indian Institute of Technology Kanpur

## Slide 2: Hardware design
Microarchitecture
Function blocks
Logic gates
Circuits
Transistors
Algorithm
Represent in HDL
HDL compiler
Simulate
Synthesize

## Slide 3: HDLs
Hardware description languages
  Offers an abstract language for representing computation that needs to be realized in hardware
  Verilog
    C-like syntax
    We will use this
  VHDL
    VHSIC HDL
    Very high speed integrated circuit HDL
    Ada-like syntax
  BSV
    Bluespec System Verilog

## Slide 4: What is Verilog?
A Hardware description language
  Describes digital systems in a convenient way
  Faster than gate-level simulation
  Still models the hardware concurrency in detail
  Possible to carry out both behavioral/functional and structural simulations
  We will do only behavioral simulation
  C-like syntax
  Remember: you are designing hardware; a new variable means you just added a new signal to your circuit
  Two major types of variables: wire and reg
  Wire used for direct communication of signals
  Reg used to store value

## Slide 5: Verilog program
A Verilog program represents the target hardware
  Usually a collection of modules
  A module is similar to a C function except that it has no return type and there can be multiple instances of a module
  All inputs and outputs are module arguments
  The modules are arranged in a hierarchy to represent the target hardware
  Example: consider designing a four-bit adder
    A full-adder module
    A four-bit adder module that instantiates four full-adder modules and connects them properly
    A top-level module representing the environment of the four-bit adder
    The top-level module instantiates the target hardware (e.g., four-bit adder module), generates the inputs, and collects the outputs

## Slide 6: Example: Full adder
/* this module receives as input three bits and outputs the sum bit and the carry bit */
module fulladder(a,b,c,sum,carry);
input a,b,c;
output sum,carry;
wire sum,carry;
assign sum=a^b^c; // sum bit
assign carry=((a&b) | (b&c) | (a&c)); //carry bit
endmodule

## Slide 7: Example: Full adder
module fulladder_top;
reg a, b, c;
wire sum, carry;
fulladder uut(a,b,c,sum,carry);
always @(sum or carry)
begin
$display("time=%d: %b + %b + %b = %b, carry = %b\n",$time,a,b,c,sum,carry);
end
initial
begin
#40
$finish;
end
initial
begin
a = 0; b = 0; c = 0;
#5
a = 0; b = 1; c = 0;
#5
a = 1; b = 0; c = 1;
#5
a = 1; b = 1; c = 1;
end
endmodule

## Slide 8: Full adder output
time=0: 0 + 0 + 0 = 0, carry = 0
time=5: 0 + 1 + 0 = 1, carry = 0
time=10: 1 + 0 + 1 = 0, carry = 1
time=15: 1 + 1 + 1 = 1, carry = 1

## Slide 9: Verilog syntax
A concurrent language
  assign a = ~b;
  assign c = d;
  Both take place concurrently
Combinational logic
  Use assign statements
  AND, OR, NOT, XOR, … (&, |, ~, ^, …)
    assign x = (a & ~b) | (~a & b);
    assign y = a ^ b;
  LHS signal must be declared as a wire (cannot hold value; values can be held only in sequential logic)
  You can use == and != (but remember this will create a comparator in hardware)
    assign x = (opcode==6’h4);

## Slide 10: Combinational logic
Four data values
  0, 1, x, z
  Possible to specify data representation format: most commonly used are binary and hex
  Possible to specify width of data (always in number of bits independent of the representation)
    6’b100101, 6’h25
Do not use +, -, <<, >> carelessly
  These are costly hardware
Never use *, /
  If you must multiply or divide, implement one (e.g. Booth’s algorithm)

## Slide 11: Combinational logic
2-input AND
  module and (x, y, out);
  input x;
  input y;
  output out; wire out; /* Note: type specification of output */
  assign out = x & y;
  endmodule
2-input NAND
  module nand (x, y, out);
  input x;
  input y;
  output out; wire out;
  assign out = ~(x & y);
  endmodule

## Slide 12: Combinational logic
A more realistic simulation of CMOS AND (structural simulation)
  module and (x, y, out);
  input x;
  input y;
  output out; wire out;
  wire a;
  nand my_nand (.x(x), .y(y), .out(a));
  assign out = ~a;
  endmodule

## Slide 13: Combinational logic
3-input OR
  module OR3 (a, b, c, z);
  input a;
  input b;
  input c;
  output z; wire z;
  assign z = a | b | c;
  endmodule
3-input NOR
  module NOR3 (a, b, c, z);
  input a; input b; input c; output z; wire z; wire w;
  OR3 level_one_or (.a(a), .b(b), .c(c), .z(w));
  assign z = ~w;
  endmodule

## Slide 14: Busses
Handles multiple bits in parallel
  8 2-input ANDs (this is not 8-input AND)
  module AND8 (x, y, z);
  input [7:0] x;
  input [7:0] y;
  output [7:0] z; wire [7:0] z;
  assign z = x & y;
  endmodule
In programming language terms it is an array of signals

## Slide 15: Sequential logic
How does a D flip-flop work?
  module DFF (d, q, clk);
  input d;
  input clk;
  output q;
  reg q;
  always @(posedge clk) begin
  q <= #2 d;
  end
  endmodule
Did we make any assumption regarding clock period here?
Can put multiple non-blocking assignments in the same always block

## Slide 16: Sequential logic
Always use non-blocking assignment <=
Always use a delay before RHS (avoid race-through and anyway that’s how things work)
LHS must be a reg
Hoist as much combinational logic as possible outside always blocks
Can use negedge also if that is the intended behavior
What’s wrong with the following?
  #2 q <= d;
Combinational always blocks are also possible

## Slide 17: Control flow
What is control flow in hardware?
  Simple example is multiplexer (if-else)
  Use if-else inside always blocks
    if-else cannot be used outside always or initial blocks
  Example: DFF with synchronous reset
  module DFF_r (d, q, r, clk);
  input d; input r; input clk;
  output q;
  reg q;
  always @(posedge clk) begin
  if (r==1’b1) begin
  q <= #2 1’b0;
  end
  else begin
  q <= #2 d;
  end
  end
  endmodule

## Slide 18: Control flow
What is control flow in hardware?
  Simple example is multiplexer (if-else)
  Use if-else inside always blocks
    if-else cannot be used outside always or initial blocks
  Example: DFF with asynchronous reset
  module DFF_r (d, q, r, clk);
  input d; input r; input clk;
  output q;
  reg q;
  always @(posedge clk or posedge r) begin
  if (r==1’b1) begin
  q <= #2 1’b0;
  end
  else begin
  q <= #2 d;
  end
  end
  endmodule

## Slide 19: Control flow
What is control flow in hardware?
  Simple example is multiplexer (if-else)
  Use if-else inside always blocks
    if-else cannot be used outside always or initial blocks
  Example: DFF with asynchronous reset (using ternary operator)
  module DFF_r (d, q, r, clk);
  input d; input r; input clk;
  output q;
  reg q;
  always @(posedge clk or posedge r) begin
  q <= #2 (r == 1’b1) ? 1’b0 : d;
  end
  endmodule

## Slide 20: Example: JK flop
/* MODULE TO SIMULATE A JK FLIP-FLOP WITH DIRECT RESET */
`define TICK #2 //Flip-flop time delay 2 units
module jkflop(j,k,clk,rst,q);
input j,k,clk,rst;
output q;
reg q;

## Slide 21: Example: JK flop
// module jkflop continues
always @(posedge clk or posedge rst) begin
if (rst==1) begin
q <= 0; // The reset normally has negligible delay and hence ignored
end
else if (j==1 & k==1) begin
q <=`TICK ~q; //Toggles
end
else if (j==1 & k==0) begin
q <= `TICK 1; //Set
end
else if (j==0 & k==1) begin
q <= `TICK 0; //Cleared
end
end
endmodule

## Slide 22: Example: JK flop
/* ENVIRONMENT FOR JK FLIP-FLOP */
module jkflop_top;
reg j,k,clk,rst;
wire q;
jkflop uut(j,k,clk,rst,q); // Unit under test
//Always at rising edge of clock display the status of flip-flop
always @(posedge clk)begin
$display(“<%d>: j=%b,k=%b,clk=%b,rst=%b,q=%b",$time,j,k,clk,rst,q);
end
//Module to generate clock with period 10 time units
initial begin
forever begin
clk=0;
#5
clk=1;
#5
clk=0;
end
end

## Slide 23: Example: JK flop
//Sample test values to run simulation (module jkflop_top continues)
initial begin
j=0; k=0; rst=1;
#4
j=1; k=1; rst=0;
#50
j=0; k=1; rst=0;
#20
j=1; k=1; rst=0;
end
//Carry out simulation for 100 units of time
initial begin
#100
$finish;
end
endmodule

## Slide 24: JK flop output
< 5>: j=1,k=1,clk=1,rst=0,q=0
< 15>: j=1,k=1,clk=1,rst=0,q=1
< 25>: j=1,k=1,clk=1,rst=0,q=0
< 35>: j=1,k=1,clk=1,rst=0,q=1
< 45>: j=1,k=1,clk=1,rst=0,q=0
< 55>: j=0,k=1,clk=1,rst=0,q=1
< 65>: j=0,k=1,clk=1,rst=0,q=0
< 75>: j=1,k=1,clk=1,rst=0,q=0
< 85>: j=1,k=1,clk=1,rst=0,q=1
< 95>: j=1,k=1,clk=1,rst=0,q=0

## Slide 25: Combinational always
All read signals must appear in sensitivity list
Same set of LHS on all paths
All cases must be covered (otherwise state-holding)
This is the only convenient way of writing a large multiplexer
An example of a non-combinational always block:
  always @(sel or a) begin
  if (sel==2’b0) begin
  z = 1’b0;
  end
  else if (sel==2’b1) begin
  z = a;
  end
  end

## Slide 26: Blocking assignments
Use of blocking assignment “=“ inside always block
  Executes before the next assignment can begin
  Unlike non-blocking assignment “<=“ where all RHS signals are evaluated simultaneously
  Example:
  always begin
  C = 1;
  A <= C;
  B = C;
  end

## Slide 27: Case statement
Helps in simulating wide multiplexors
  always @(sel or a or b or c) begin
  case (sel)
  2’b00: z = a;
  2’b01: z = b;
  2’b10: z = c;
  default: z = 1’bx; // Note that x is a constant here
  // (don’t care)
  endcase
  end

## Slide 28: Concatenation
Syntax: R{E1, E2,…, En} means R repetitions of concatenation of E1, …, En.
  reg [15:0] a;
  reg [31:0] b;
  wire [31:0] out;
  assign out = {16{a[15]}, a} + b;

## Slide 29: Register file/memory
Essentially a 2D array of “signals”
  reg [31:0] register_file [0:7];
  wire [31:0] rf_bus;
  wire r2b4;
  assign rf_bus = register_file [2];
  assign r2b4 = rf_bus[4];
Cannot do register_file[2][4]; (this is illegal because this is not how memory works)

## Slide 30: Tri-state
Use of the z state
  reg [31:0] mem [0:7];
  wire [2:0] a;
  wire [31:0] d;
  wire read_enable;
  assign d = read_enable ? mem[a] : 32’bz;

## Slide 31: Extra hardware
Think while writing your program
  You are building a hardware, not software
  always @(posedge clk) begin
  if (x) begin
  z <= #2 a + b;
  end
  else if (y) begin
  w <= #2 a + b;
  end
  else begin
  r <= #2 a + b;
  end
  end

## Slide 32: Verilog is concurrent
The big difference with C (get used to it)
  initial begin
  a = 1’b0;
  b = 1’b0;
  end
  always @(posedge clk) begin
  a <= #1 1’b1;
  b <= #1 a;
  end
  What are the waveforms of a and b? (assume clk is 10 units and 50% duty cycle)

## Slide 33: Built-in functions
Very useful for debugging
  Can use $display to print signals (allowed inside always and initial blocks)
  Can use $monitor to catch changes on signals (allowed inside initial blocks only)
  $time returns verilog’s in-built clock time
  $finish terminates simulation

## Slide 34: Verilog preprocessor
Just like C, minor difference in syntax
  `define store_opcode 6’h4
  `define TICK #2
  `include “opcodes.h”
  always @(posedge clk) begin
  q <= `TICK d;
  end

## Slide 35: Register or wire?
General confusion: how do I decide if a signal should be declared as a reg or a wire?
  Forget about the programming language and think about the hardware
  If in the hardware something turns out to be a wire, it should be declared as wire and driven every cycle (otherwise it becomes Z or X)
  Otherwise make it reg (state holding)

## Slide 36: Verilog tips
Suppose module M has an output Q of type reg
Module M’ instantiates M and passes a reg R for Q
This is illegal
  A very common mistake observed in beginners
  Illegal because this instantiation implicitly connects a register to another register without specifying a clock
Can connect only a wire to a register through instantiation
  This will make sense if you think about the hardware
Module M’ can only pass a wire for Q

## Slide 37: Verilog tips
If the LHS of an assignment is a reg, use non-blocking assignment i.e., <=
  This will generate flip-flops, which is what we want
  Blocking assignment inside always block is typically used to model combinational logic only
  Careless use of blocking assignment inside always blocks can lead to generation of latches
  Latches are difficult to handle in terms of timing

## Slide 38: Verilog tips
If there are non-blocking assignments inside an always block, make the logic edge-triggered
  This will generate flip-flops as opposed to latches
  Use posedge or negedge clock as the triggering signal as opposed to posedge or negedge of some other signals
    Leads to cleaner and simpler circuits because all flip-flops can have a common clock

## Slide 39: Verilog tips
Avoid always blocks as much as possible and do as much computation combinationally as possible
  Leads to smaller compact circuits