## Slide 1: Instruction Set Architecture
Mainak Chaudhuri
Indian Institute of Technology Kanpur

## Slide 2: Sketch
What is instruction set architecture (ISA)?
Computer operations
Operands
Logical operations
Operations for making decision
Procedure/Function calls
Instruction encoding
Manipulating strings
Floating-point instructions
Translating and starting a program

## Slide 3: What is ISA?
Operations of a computer are done through instructions
  One instruction does one operation
Set of instructions supported by a computer is the instruction set of the computer
Organization of the computer defined by the instruction set is the instruction set architecture (ISA) of the computer
The guiding principle in designing ISA is that the implementation of the ISA should be simple
The programming language that uses instructions of a computer is called an assembly language

## Slide 4: Computer operations
Every computer must be able to do arithmetic operations
  Add, subtract, multiply, divide
  The variables operated on and the result variables are called operands
    The operands used in an operation are called source operands or read operands
    The operands used for storing the result of an operation are called destination operands or write operands
    c = a + b: a and b are source or read operands, c is the destination or write operand
    Most computers allow at most two sources and one destination per instruction

## Slide 5: Computer operations
Consider the MIPS instruction “add a, b, c”
  MIPS is the name of a processor family
    We will understand what MIPS stands for later in the course
  “add” is the name of the instruction which defines the operation to be done when this instruction is encountered by the computer
  Among the three operands (a, b, c), the one right after “add” is the destination operand
    Usually the destination operand is mentioned right after the operation name
  Other two operands (b, c) are source operands
  Add b and c, put the result in a

## Slide 6: Computer operations
The MIPS add instruction can be used to generate an instruction sequence for adding a larger number of operands
  Consider adding b, c, d, e and storing the result in a (C language statement: a = b+c+d+e;)
    add a, b, c
    add a, a, d
    add a, a, e
A compiler (e.g., gcc) generates a sequence of instructions from a HLL (e.g., C) program
  Each instruction specifies one operation
  The program containing this sequence of MIPS instructions is called a MIPS assembly language program

## Slide 7: Computer operations
More examples on translating C statements into MIPS assembly language
  Consider the C statements
    a = b + c;
    d = a – e;
  Translation in MIPS assembly language
    add a, b, c
    sub d, a, e
  Notice the use of the instruction “sub”
  Notice that we have implicitly assumed that the MIPS instruction operands have the same name as the C statement variables
    This is usually not the case; we will clarify soon

## Slide 8: Computer operations
More examples on translating C statements into MIPS assembly language
  Consider the same C statements written as
    d = (b + c) – e;
  MIPS translation
    add d, b, c
    sub d, d, e
  Consider the C statement
    f = (g + h) – (i + j);
  MIPS translation may require storing the results of two additions in two temporary variables
    add t0, g, h
    add t1, i, j
    sub f, t0, t1

## Slide 9: Computer operations
Summary
  Computer operations come in many types
    We have discussed a few and will discuss many more
  Each distinct operation has a corresponding instruction that the computer understands
  Each operation has a few operands
    Usually three in most computers
    Two are source operands and one is destination operand
    Accordingly, each instruction has a corresponding number of operands
    In a computer, all instructions may have the same number of operands or may have a variable number of operands
      Simple designs favor uniformity and regularity in instructions

## Slide 10: Operands
So far we have assumed that instruction operands are same as HLL program variables
  This assumption is incorrect
  Each hardware operation reads its source operands from some storage and writes its destination operand to some storage
    This storage can be either a register from the register file inside the processor or a memory location
      By memory we usually mean RAM of the computer (DRAM)
      Recall that anything that is accessed from DRAM is also copied into SRAM cache inside the processor replacing something if the SRAM cache is already full
      So, at any point in time, the SRAM cache stores a subset of the DRAM contents
      The data in a memory location can be found in SRAM cache or in DRAM (DRAM is accessed only if SRAM cache does not have the data)

## Slide 11: Operands
Translating an HLL program to an assembly language program involves two basic steps
  Mapping HLL operators to computer instructions
    Exact instruction names differ from one computer to another, but the operations done by the instructions are largely same
  Mapping HLL operands (or variables) to computer instruction operands
    Requires deciding which variable is stored where and when
    Every variable gets a fixed memory location
      However, this forces every computer instruction to operate on memory operands only and obviates the need for a register file
      But accessing a register is faster than accessing memory (faster than even SRAM cache)

## Slide 12: Operands
Mapping variables to operands
  Fast access to registers motivates mapping variables to register operands
  Simplicity of design also motivates restricting the operands of certain instructions to registers only
    Consistent latency of these operations (recall that accessing memory can have variable latency)
    In MIPS, many instructions (including arithmetic) allow only register operands
    In x86, both register and memory operands are allowed
      Makes instruction latency variable
  Width of register file dictates the width of a register operand (usually 32 or 64 bits)
    Dictates the width of datapath used in computation

## Slide 13: Operands
Mapping variables to operands
  Register width is typically decided based on the primitive variable types used in HLL programs
    Makes it easy to map variables to registers
    In C language, these are char, short, int, long long, float, double
    Notice that 64-bit registers are large enough to hold a variable of any of these types
    Since wider register file is slower, it is important to find out how often a 64-bit operand is used
      If that is not too common, a 32-bit wide register file would suffice
      A 64-bit operand will have to be mapped on a pair of registers and may require double the 32-bit access time
      Important design principle: make the common case fast

## Slide 14: Operands
Mapping variables to operands
  Since taller register file is slower, the number of registers must be restricted
  Since each variable is given a unique memory location to store its value, it must be copied to a register if an instruction wants to use it as a register operand
    In MIPS, arithmetic and many other instructions only allow register operands
  Not all variables of a program can be allocated in registers at the same time due to restricted number of registers
    Variables are allocated in and de-allocated from registers as the program progresses (filled from and spilled into memory)

## Slide 15: Operands
Mapping variables to operands
  Register allocation of variables is the compiler’s responsibility
    Goal is to minimize the number of fills and spills because memory access is inefficient
    Example: assume four registers r1, r2, r3, r4
    Consider the C statements:
      a=b + c; // Allocate a, b, c to r1, r2, r3
      d=e + f; // Allocate d to r4, how to allocate e and f?
      a=a + d;
      b=a + e;

## Slide 16: Operands
Mapping variables to operands
    Consider the C statements:
      a=b + c; // Allocate a, b, c to r1, r2, r3
      d=e + f; // Allocate d to r4, how to allocate e and f?
      a=a + d;
      b=a + e;
    Assembly language translation (not exactly MIPS)
      load r2, addr_b #fill b
      load r3, addr_c #fill c
      add r1, r2, r3 #a = b + c
      load r2, addr_e #fill e
      load r3, addr_f #fill f
      add r4, r2, r3 #d = e + f
      add r1, r1, r4 #a= a + d
      add r3, r1, r2 #b=a + e
      store r1, addr_a #spill a (note changed syntax)
      store r3, addr_b #spill b
      store r4, addr_d #spill d

## Slide 17: Operands
Mapping variables to operands
  Large number of registers not only increase the access time of register operands, but also can increase the clock cycle time
    Depends on how much work needs to be done within a clock cycle
    Cycle time could be register read time + latency of combinational operation + setup time of register + register write time + clock skew time
      Notice that in this formulation, the propagation delay of registers is not important
    Register read, computation of the operation, and register write can be split into three consecutive cycles
      The cycle time will decrease compared to the previous one, but will remain limited by max(read latency, op latency, write latency)

## Slide 18: Operands
Mapping variables to operands
  MIPS assembly language denotes registers using the $ sign followed by the register name or number (e.g., $0, $1, …, $31 for 32 registers)
    The book uses a different notation: allocates the program variables in registers $sN where N is an integer and any temporary variable in registers $tN
      Makes sure that the total number of registers never exceeds 32 because MIPS instruction set defines only 32 registers
    Consider compiling f = (g + h) – (i + j);
    Assume that f, g, h, i, j are allocated to $s0, $s1, $s2, $s3, $s4
      add $t0, $s1, $s2
      add $t1, $s3, $s4
      sub $s0, $t0, $t1

## Slide 19: Operands
Mapping variables to operands
  For instructions that have two register sources and one register destination, the best performance is achieved if the register file has two read ports and one write port
    Two reads can be done in parallel
    If the register file had a single read port, this would have required two sequential accesses doubling the overall time to read the source operands
    If we assume that one instruction executes at a time, the write port can share the decoder, wordline and the bitline with one of the read ports
      This is called an RW port (supports both read and write)
      This assumption is usually not true and we will lift this assumption later

## Slide 20: Operands
Fill and spill instructions in MIPS require memory and register operands
Other ISAs (such as x86) allow even arithmetic instructions to have memory operands
Memory operands essentially need to specify a memory address
  Just like register operands specify a register name (which translates to a register number or register address)
  Since the number of registers is small, it is easy to specify a register address (requires few bits)
    Number of bits required: log of number of registers

## Slide 21: Operands
Memory operands essentially need to specify a memory address
  Since instructions need to be stored in memory, it is important to be economical in specifying operands
  Having 4 GB memory would require 32 bits of address to specify a memory operand
    Not particularly attractive (called direct memory addressing mode)
    Recall that instructions are generated by the compiler and the compiler does not always know the addresses of all variables of a program
      Think about the return pointer of a malloc call (resolved only when the program runs)

## Slide 22: Operands
Memory operands essentially need to specify a memory address
  Memory operand addresses are usually specified relative to a base register
    100($2) is interpreted as (100 + contents of $2) and the result is taken as the address of a memory operand
    The instruction could be “load $1, 100($2)”
      Fills register $1 with the contents at address (100 + $2)
    Known as displacement mode of memory addressing
      The constant 100 is called the displacement and can be positive or negative
      The register $2 is known as the base register (can use any register as the base register)

## Slide 23: Operands
Displacement mode of memory addressing
  Very useful in walking through an array or a structure
    The starting address of the array can be stored in the base register and the displacement can be gradually incremented
    The starting address of a structure can be stored in the base register and the displacement can specify the offset to the field of the structure to be accessed
  This is the only supported mode of addressing memory in MIPS

## Slide 24: Operands
Memory operands are filled (or loaded) into registers before they can be operated on and the register contents can be spilled (or stored) to memory
  Memory operands are represented by a memory address which refers to a byte and a register is typically bigger than a byte
    Four- or eight-byte registers in most ISAs
    Need to disambiguate this size mismatch
  To resolve this, data transfer instructions also specify the number of bytes to be transferred between register and memory
    Loads and stores come in different flavors in MIPS

## Slide 25: Operands
Memory operand size
  MIPS has four different load and four different store instructions corresponding to four different size
    Load byte: lb
    Load half word: lh (loads two bytes)
    Load word: lw (loads four bytes)
    Load double word: ld (supported in 64-bit MIPS)
    Store byte: sb
    Store half word: sh
    Store word: sw
    Store double word: sd (supported in 64-bit MIPS)

## Slide 26: Operands
Memory operand size
  In x86 ISA, an instruction may have multiple memory operands
    Not possible to encode memory operand size in instruction name because different memory operands may have different sizes within the same instruction
      Load a byte from address A, load a word from address B, add them, and store the result in a register
    Each memory operand needs to specify its size separately within the instruction
      Requires more bits in the instruction (e.g., could be two bits per memory operand)

## Slide 27: Operands
Sub-word memory operands in 32-bit MIPS
  Consider the load byte or load half word instruction
    These instructions load a byte or two bytes into the least significant side of the destination register
    What about the remaining bits of the destination register?
      Two options: zero-filled or sign-extended
      Sign-extension fills the remaining bits with the sign bit of the loaded byte or the loaded half word
      Notice that in two’s complement representation, extending a number’s sign bit by arbitrary number of bits does not change the equivalent decimal value of the number
      Introduces two more flavors for sub-word loads
        Load byte unsigned (lbu) and load byte (lb); load half unsigned (lhu) and load half (lh);
        Unsigned flavor fills the remaining bits of the destination register with zeros; the other one sign-extends

## Slide 28: Operands
When does the compiler generate which load instruction?
  Consider the following C code snippet
    long long x[10];
    long long y = x[2];
  In 64-bit MIPS, the assignment statement will generate a ld instruction
    If y is allocated to $1 and the starting address of x is in $29, the compiler will generate ld $1, 16($29)
    Each element of x is eight bytes
  In 32-bit MIPS, the assignment statement will generate two lw instructions
    Assume that y is split into two registers $1 and $2
    lw $1, 16($29)
    lw $2, 20($29)

## Slide 29: Operands
When does the compiler generate which load instruction?
  Consider the following C code snippet
    int x[10];
    int y = x[2];
  The assignment statement will generate a lw instruction
    If y is allocated to $1 and the starting address of x is in $29, the compiler will generate lw $1, 8($29)
    Each element of x is four bytes

## Slide 30: Operands
When does the compiler generate which load instruction?
  Consider the following C code snippet
    short x[10];
    short y = x[2];
  The assignment statement will generate a lh instruction
    If y is allocated to $1 and the starting address of x is in $29, the compiler will generate lh $1, 4($29)
    Each element of x is two bytes

## Slide 31: Operands
When does the compiler generate which load instruction?
  Consider the following C code snippet
    unsigned short x[10];
    unsigned short y = x[2];
  The assignment statement will generate a lhu instruction
    If y is allocated to $1 and the starting address of x is in $29, the compiler will generate lhu $1, 4($29)
    Each element of x is two bytes

## Slide 32: Operands
When does the compiler generate which load instruction?
  Consider the following C code snippet
    char x[10];
    char y = x[2];
  The assignment statement will generate a lb instruction
    If y is allocated to $1 and the starting address of x is in $29, the compiler will generate lb $1, 2($29)
    Each element of x is one byte

## Slide 33: Operands
When does the compiler generate which load instruction?
  Consider the following C code snippet
    unsigned char x[10];
    unsigned char y = x[2];
  The assignment statement will generate a lbu instruction
    If y is allocated to $1 and the starting address of x is in $29, the compiler will generate lbu $1, 2($29)
    Each element of x is one byte

## Slide 34: Operands
Sub-word memory operands in 32-bit MIPS
  Store byte and store half word do not have the unsigned or signed flavors
    Store byte instruction takes the least significant byte from the source register (left operand) and stores the byte at the address of the memory operand
    sb $2, 0($1)
    Store half word instruction takes the least significant two bytes from the source register (left operand) and stores the bytes starting at the address of the memory operand
    sh $2, 0($1)
    There is no scope of zero-fill or sign-extension

## Slide 35: Operands
When does the compiler generate which store instruction?
  Consider the following C code snippet
    unsigned char x[10];
    unsigned char y;
    x[2] = y;
  The assignment statement will generate a sb instruction
    If y is allocated to $1 and the starting address of x is in $29, the compiler will generate sb $1, 2($29)
    Each element of x is one byte
  Changing type to “char” does not change the instruction
    Bit#7 of y already encodes the sign (LSB is bit#0)

## Slide 36: Operands
When does the compiler generate which store instruction?
  Consider the following C code snippet
    unsigned short x[10];
    unsigned short y;
    x[2] = y;
  The assignment statement will generate a sh instruction
    If y is allocated to $1 and the starting address of x is in $29, the compiler will generate sh $1, 4($29)
    Each element of x is two bytes
  Changing type to “short” does not change the instruction
    Bit#15 of y already encodes the sign (LSB is bit#0)

## Slide 37: Operands
When does the compiler generate which store instruction?
  Consider the following C code snippet
    unsigned int x[10];
    unsigned int y;
    x[2] = y;
  The assignment statement will generate a sw instruction
    If y is allocated to $1 and the starting address of x is in $29, the compiler will generate sw $1, 8($29)
    Each element of x is four bytes
  Changing type to “int” does not change the instruction
    Bit#31 of y already encodes the sign (LSB is bit#0)

## Slide 38: Operands
When does the compiler generate which store instruction?
  Consider the following C code snippet
    unsigned long long x[10];
    unsigned long long y;
    x[2] = y;
  The assignment statement will generate a sd instruction in 64-bit MIPS
    If y is allocated to $1 and the starting address of x is in $29, the compiler will generate sd $1, 16($29)
    Each element of x is eight bytes
  Changing type to “long long” does not change the instruction
    Bit#63 of y already encodes the sign (LSB is bit#0)

## Slide 39: Operands
When does the compiler generate which store instruction?
  Consider the following C code snippet
    unsigned long long x[10];
    unsigned long long y;
    x[2] = y;
  The assignment statement will generate two sw instructions in 32-bit MIPS
    If y is split into $1 and $2 and the starting address of x is in $29, the compiler will generate the following
    sw $1, 16($29)
    sw $2, 20($29)

## Slide 40: Operands
Alignment of memory operands
  MIPS requires that a memory operand of size n bytes must start at an address that is divisible by n
    The least significant log(n) bits of the memory operand address must be zero
    Observe that byte operands (n==1) can start at any address
      This is a property of byte-addressable memory
      Each memory address corresponds to a distinct byte
    Observe that n can take only a few values: 1, 2, 4, 8
  x86 ISA allows unaligned memory operands

## Slide 41: Operands
Alignment of memory operands
  What can be the reason for this alignment requirement?
    Observe that DRAM row sizes and interface between the SRAM cache and the DRAM controller are powers of two and are usually bigger than the largest n
      Therefore, DRAM row sizes and SRAM cache to DRAM controller interface sizes are divisible by n
    If a half word memory operand starts at an odd address, there is a chance that it may get split across two DRAM rows or two transactions between SRAM cache and DRAM controller
      This will double the operand fill time because this will require activating two DRAM rows one after another or making two transactions to the DRAM controller
    Similar arguments apply for word and double word operands

## Slide 42: Operands
Byte ordering within a memory word
  Suppose we are loading a half word from address zero
    We need to load two bytes from addresses 0 and 1
    Which of these is the least significant byte?
      Decided by how the bytes are ordered within a word i.e., how you assign addresses to bytes within a word
      The word containing the half word to be loaded starts at address zero and ends at address 3; need to assign these four addresses (0, 1, 2, 3) to the bytes in a word
      It is possible to do this assignment in 4! ways
      Out of these 24 different orders, only two are sequential in nature; in one case, the most significant byte has address 0 and the address increases linearly till the least significant byte gets address 3 (called big endian ordering); in the other case, the least significant byte gets address 0 and the address increases linearly till the most significant byte gets address 3 (called little endian ordering)

## Slide 43: Operands
Byte ordering within a memory word
  Endianness depends on where the address 0 is within a word
    If address 0 is at the most significant byte (the big end), it is called big endian
    If address 0 is at the least significant byte (the little end), it is called little endian
    MIPS follows big endian ordering
    x86 follows little endian ordering
  It is important to know the endianness of a machine if you are trying to write program to communicate between two machines
    If the machines have different endianness, extra effort needed on the receiving side

## Slide 44: Operands
Word ordering within a double word
  Two words in a double word
    Let the addresses of the words be zero and one
  Big endian machines have word#0 as the most significant word and word#1 as the least significant word
  Little endian machines have word#0 as the least significant word and word#1 as the most significant word

## Slide 45: Operands
Example C code to distinguish between big endian and little endian ISAs
    unsigned int x = 0x12345678;
    unsigned char y = *(char*)&x; // byte at start address
    printf(“%#x\n”, y);
  A big endian machine would print 0x12
  A little endian machine would print 0x78
12
34
56
78
&x
&x + 1
&x + 2
&x + 3
Address
Value
Big endian
12
34
56
78
&x + 3
&x + 2
&x + 1
&x
Little endian

## Slide 46: Operands
How to do unaligned memory operand accesses in MIPS?
  Is it really important?
  Suppose I would like to extract four consecutive characters starting from any arbitrary location of a string, say, “abcdefghij”
    For example, I may want to extract “defg”, which starts at an unaligned word address
      One option is to do four load byte operations and then somehow put them together properly in a 32-bit register
        A lot of instructions needed
      Slightly better option is to do two load bytes (for ‘d’ and ‘g’) and one load half word (for “ef”)
        Still a lot of instructions needed
  Supporting unaligned access is important for reducing the number of instructions in a program

## Slide 47: Operands
MIPS supports two unaligned load word instructions and two unaligned store word instructions
  lwl (load word left)
  lwr (load word right)
  swl (store word left)
  swr (store word right)

## Slide 48: Operands
Understanding lwl and lwr
  Example: lwl $4, 0($10); let $10 contain 0x57
    Let the word containing this byte address be w
    Extract the bytes contained by w that start from this address (remember this is big endian)
    Put these bytes (in this case one byte) in the upper portion of $4 and leave the remaining bytes (in this case 3 lower bytes) unchanged
  Example: lwr $4, 0($10); let $10 contain 0x5a
    Extract the bytes contained by w that end at this address
    Put these bytes (in this case three bytes) in the lower portion of $4 and leave the remaining bytes (in this case the upper byte) unchanged

## Slide 49: Operands
When should the compiler generate lwl and lwr?
  Suppose the char pointer x points to “abcdefghij” i.e., char x[10] = “abcdefghij”
  If we want to extract “defg”, the compiler will generate an lwl from address x+3 and an lwr from address x+6
    int y = *((int*)&x[3]);

## Slide 50: Operands
Handling constant operands
  Compiling a = b + 3 where a and b are integers
    Suppose a is allocated to $11, b is allocated to $12, and the constant 3 is allocated to $13
    Suppose the address of a is 0($1), address of b is 0($2), and address of 3 is 0($3)
      lw $12, 0($2)
      lw $13, 0($3)
      add $11, $12, $13
      sw $11, 0($1)
  Observe that allowing constant operands in instructions can eliminate loading constants from memory
    These are called immediate operands

## Slide 51: Operands
Handling constant operands
  The addi instruction allows one of the two source operands to be an immediate
    The add immediate instruction
    Compilation of a = b + 3 is the following
      lw $12, 0($2)
      addi $11, $12, 3
      sw $11, 0($1)
  Immediate operands can be negative also
    There is no need to have a subi instruction
  The constant zero is a very common operand
    Also, copying a value from one register to another can be compiled as an addi instruction with zero as an immediate operand
    MIPS dedicates register $0 to always hold the value 0

## Slide 52: Operands
Example uses of $0
  How to compile a = 3 – b
    Suppose a is allocated to $11, b is allocated to $12
    Suppose the address of a is 0($1), address of b is 0($2)
      lw $12, 0($2)
      sub $12, $0, $12
      addi $11, $12, 3
      sw $11, 0($1)
    Alternate compilation (requires one extra register)
      lw $12, 0($2)
      addi $13, $0, 3
      sub $11, $13, $12
      sw $11, 0($1)

## Slide 53: Operands
Summary
  Three types of operands: register operands, memory operands, immediate operands
  Register operands are represented by register names and register names have one-to-one mapping to register numbers
    MIPS ISA has 32 distinct registers
    Out of these, one register is hardwired to store zero
  Memory operands use displacement addressing mode in MIPS
    A memory operand address is represented as the sum of a base register content and a displacement
    Displacement can be positive or negative
  Immediate operands represent constants

## Slide 54: Logical operations
So far we have seen only arithmetic operations
  Addition, Subtraction (add, sub, addi in MIPS)
  Computers also support multiplication and division operations (mult, div in MIPS)
Logical operations operate on bits of the operands
  Operands can be either registers or immediates
  Some of the MIPS logical instructions: and, or, nor, xor, andi, ori, xori, sll (shift left logical), srl (shift right logical), sra (shift right arithmetic), sllv (shift left logical variable), srlv, srav

## Slide 55: Logical operations
Bit-wise logical operators of C nicely map to the logical operations supported by MIPS
  &, |, ^ map to and, or, xor
    If one operand is immediate, andi, ori, xori are generated
  MIPS does not have a “not” instruction
    To maintain the uniformity in number of operands
  The nor instruction can be used to compile ~
    If one operand is zero, nor is equivalent to not

## Slide 56: Logical operations
Bit-wise logical operators of C nicely map to the logical operations supported by MIPS
  >> maps to srl or sra or srlv or srav depending on the type of the operand being shifted and the shift amount
    If the operand being shifted is of unsigned type, the srl or srlv instruction is generated
      Zeros are shifted into the most significant side
      If the shift amount is a constant and at most 31, the srl instruction is generated
      If the shift amount is larger or a variable, the srlv instruction is generated where the shift amount is specified in a register
      In both cases, shifting right by one bit position is equivalent to dividing by two (integer division)

## Slide 57: Logical operations
Bit-wise logical operators of C nicely map to the logical operations supported by MIPS
  >> maps to srl or sra or srlv or srav depending on the type of the operand being shifted and the shift amount
    If the operand being shifted is of signed type, the sra or srav instruction is generated
      Sign bit is shifted into the most significant side so that the shifted result retains appropriate sign of the operand
      If the shift amount is a constant and at most 31, the sra instruction is generated
      If the shift amount is larger or a variable, the srav instruction is generated where the shift amount is specified in a register

## Slide 58: Logical operations
Bit-wise logical operators of C nicely map to the logical operations supported by MIPS
  << maps to sll or sllv depending on the shift amount
    Always zeros are shifted into the least significant side
    Shifting by one bit position is equivalent to multiplying by two

## Slide 59: Logical operations
Example compilation
  Suppose a, b, c are allocated to registers $11, $12, $13 and their memory addresses are in $1, $2, $3
    int a, b, c; lw $12, 0($2)
    lw $13, 0($3)
    a = b ^ c; xor $11, $12, $13
    b = a & c; and $12, $11, $13
    a = c | a; or $11, $13, $11
    b = ~a; nor $12, $11, $0
    b = b ^ 0x20; xori $12, $12, 0x20
    a = b & 0x7; andi $11, $12, 0x7
    sw $11, 0($1)
    sw $12, 0($2)
    sw $13, 0($3)

## Slide 60: Logical operations
Example compilation
  Suppose a, b, c are allocated to registers $11, $12, $13 and their memory addresses are in $1, $2, $3
    int a, b; lw $12, 0($2)
    unsigned int c; lw $13, 0($3)
    a = b >> 12; sra $11, $12, 12
    c = c >> 4; srl $13, $13, 4
    b = b >> c; srav $12, $12, $13
    c = c >> b; srlv $13, $13, $12
    c = c*8; sll $13, $13, 3
    b = a << c; sllv $12, $11, $13
    sw $11, 0($1)
    sw $12, 0($2)
    sw $13, 0($3)

## Slide 61: Operations for making decision
Interesting programs decide the execution path based on the computation results
  In C language, these are expressed using if-else if-else blocks
  Involves evaluating a condition and taking one of the two possible paths of execution
    Fall through or jump
    The basic operation used in evaluating a condition is comparison
      if (x == y) z++; // Fall through path
      else z--; // Jump path
    MIPS ISA offers a set of instructions that can compare and jump based on the outcome of the comparison
      Known as conditional branch instructions

## Slide 62: Conditional branch instructions
MIPS ISA comes with six flavors of such instructions
  beq (Branch if equal) compares two register operands
  bne (Branch if not equal) compares two register operands
  bgez (Branch if >= 0) compares a register operand against zero
  bgtz (Branch if > 0)
  blez (Branch if <= 0)
  bltz (Branch if < 0)
  Enough to compile any condition and jump

## Slide 63: Conditional branch instructions
Sometimes it is necessary to make unconditional jumps
  C programming language has “go to” for this purpose
  MIPS ISA offers an unconditional jump instruction denoted by j

## Slide 64: Conditional branch instructions
Example compilation
  Suppose x, y, z are allocated to registers $11, $12, $13 and their addresses are in $1, $2, $3
    int x, y, z;
    if (x == y) z++;
    else z--;
    MIPS assembly language program:
    lw $11, 0($1)
    lw $12, 0($2)
    lw $13, 0($3)
    bne $11, $12, Label1
    addi $13, $13, 1
    j Label2
    Label1: addi $13, $13, -1
    Label2: sw $13, 0($3)
Branch target
Jump target

## Slide 65: Conditional branch instructions
Example compilation
  Suppose x, y, z are allocated to registers $11, $12, $13 and their addresses are in $1, $2, $3
    int x, y, z;
    if (x != y) z++;
    else z--;
    MIPS assembly language program:
    lw $11, 0($1)
    lw $12, 0($2)
    lw $13, 0($3)
    beq $11, $12, Label1
    addi $13, $13, 1
    j Label2
    Label1: addi $13, $13, -1
    Label2: sw $13, 0($3)

## Slide 66: Conditional branch instructions
Example compilation
  Suppose x, z are allocated to registers $11, $13 and their addresses are in $1, $3
    int x, z;
    if (x <= 0) z++;
    else z--;
    MIPS assembly language program:
    lw $11, 0($1)
    lw $13, 0($3)
    bgtz $11, Label1
    addi $13, $13, 1
    j Label2
    Label1: addi $13, $13, -1
    Label2: sw $13, 0($3)

## Slide 67: Conditional branch instructions
Example compilation
  Suppose x, z are allocated to registers $11, $13 and their addresses are in $1, $3
    int x, z;
    if (x < 0) z++;
    else z--;
    MIPS assembly language program:
    lw $11, 0($1)
    lw $13, 0($3)
    bgez $11, Label1
    addi $13, $13, 1
    j Label2
    Label1: addi $13, $13, -1
    Label2: sw $13, 0($3)

## Slide 68: Conditional branch instructions
Example compilation
  Suppose x, z are allocated to registers $11, $13 and their addresses are in $1, $3
    int x, z;
    if (x >= 0) z++;
    else z--;
    MIPS assembly language program:
    lw $11, 0($1)
    lw $13, 0($3)
    bltz $11, Label1
    addi $13, $13, 1
    j Label2
    Label1: addi $13, $13, -1
    Label2: sw $13, 0($3)

## Slide 69: Conditional branch instructions
Example compilation
  Suppose x, z are allocated to registers $11, $13 and their addresses are in $1, $3
    int x, z;
    if (x > 0) z++;
    else z--;
    MIPS assembly language program:
    lw $11, 0($1)
    lw $13, 0($3)
    blez $11, Label1
    addi $13, $13, 1
    j Label2
    Label1: addi $13, $13, -1
    Label2: sw $13, 0($3)

## Slide 70: Conditional branch instructions
Example compilation
  Suppose x, y, z are allocated to registers $11, $12, $13 and their addresses are in $1, $2, $3
    int x, y, z;
    if (x > y) z++;
    else z--;
    MIPS assembly language program:
    lw $11, 0($1)
    lw $12, 0($2)
    lw $13, 0($3)
    sub $14, $11, $12
    blez $14, Label1
    addi $13, $13, 1
    j Label2
    Label1: addi $13, $13, -1
    Label2: sw $13, 0($3)

## Slide 71: Conditional branch instructions
Example compilation
  Suppose x, y, z are allocated to registers $11, $12, $13 and their addresses are in $1, $2, $3
    int x, y, z;
    if (x > y) z++;
    else z--;
    Instead of a subtraction, a comparison operation can be invoked to save energy and possibly time
    The instructions slt and slti achieve this
      slt compares two source register operands and sets the destination register contents to one if the first operand is less than the second
      slti compares a source register against an immediate operand and sets the destination register contents to one if the source register operand is less than the immediate

## Slide 72: Conditional branch instructions
Example compilation
  Suppose x, y, z are allocated to registers $11, $12, $13 and their addresses are in $1, $2, $3
    int x, y, z;
    if (x > y) z++;
    else z--;
    MIPS assembly language program:
    lw $11, 0($1)
    lw $12, 0($2)
    lw $13, 0($3)
    slt $14, $12, $11
    beq $14, $0, Label1
    addi $13, $13, 1
    j Label2
    Label1: addi $13, $13, -1
    Label2: sw $13, 0($3)

## Slide 73: Conditional branch instructions
Example compilation
  Suppose x, y, z are allocated to registers $11, $12, $13 and their addresses are in $1, $2, $3
    int x, y, z;
    if (x >= y) z++;
    else z--;
    MIPS assembly language program:
    lw $11, 0($1)
    lw $12, 0($2)
    lw $13, 0($3)
    slt $14, $11, $12
    bne $14, $0, Label1
    addi $13, $13, 1
    j Label2
    Label1: addi $13, $13, -1
    Label2: sw $13, 0($3)

## Slide 74: Conditional branch instructions
Example compilation
  Suppose x, z are allocated to registers $11, $13 and their addresses are in $1, $3
    int x, z;
    if (x < 3) z++;
    else z--;
    MIPS assembly language program:
    lw $11, 0($1)
    lw $13, 0($3)
    slti $14, $11, 3
    beq $14, $0, Label1
    addi $13, $13, 1
    j Label2
    Label1: addi $13, $13, -1
    Label2: sw $13, 0($3)

## Slide 75: Conditional branch instructions
Example compilation
  Suppose x, z are allocated to registers $11, $13 and their addresses are in $1, $3
    int x, z;
    if (x <= 3) z++;
    else z--;
    MIPS assembly language program:
    lw $11, 0($1)
    lw $13, 0($3)
    slti $14, $11, 4
    beq $14, $0, Label1
    addi $13, $13, 1
    j Label2
    Label1: addi $13, $13, -1
    Label2: sw $13, 0($3)

## Slide 76: Conditional branch instructions
Example compilation
  Suppose x, z are allocated to registers $11, $13 and their addresses are in $1, $3
    int x, z;
    if (x > 3) z++;
    else z--;
    MIPS assembly language program:
    lw $11, 0($1)
    lw $13, 0($3)
    slti $14, $11, 4
    bne $14, $0, Label1
    addi $13, $13, 1
    j Label2
    Label1: addi $13, $13, -1
    Label2: sw $13, 0($3)

## Slide 77: Conditional branch instructions
Signed and unsigned comparisons
  Comparison between two 32-bit signed values and between two 32-bit unsigned values must be done differently
    The interpretation of the most significant bit is different
    For signed types, the entire 32-bit value must be treated as a two’s complement value
      The most significant bit will be multiplied by -231
    For unsigned types, the entire 32-bit value must be treated as an unsigned binary value
      The most significant bit will be multiplied by 231
    unsigned int a = 0xFFFFFFF0;
    int b = (int)a; // What is the decimal value of b?

## Slide 78: Conditional branch instructions
Signed and unsigned comparisons
    Consider the following C code
    unsigned int a = 0xFFFFFFF0;
    unsigned int b = 0xF;
    int x = 0xFFFFFFF0;
    int y = 0xF;
    int c = 0;
    if (a < b) c++;
    else c--;
    if (x < y) c++;
    else c--;
    Final value of c is zero; the two comparisons must be done differently
      In one case, the comparison operands must be treated unsigned and in the other case, they are treated signed

## Slide 79: Conditional branch instructions
Signed and unsigned comparisons
  Comparison between two 32-bit signed values and between two 32-bit unsigned values must be done differently
  MIPS ISA offers two flavors of slt and slti to convey to the hardware how the operands of the comparison must be treated
    sltu and sltiu instructions treat the comparison operands as unsigned values
    slt and slti instructions treat the comparison operands as signed values
    In the example of the last slide, the first comparison would generate the sltu instruction and the second would generate the slt instruction

## Slide 80: Conditional branch instructions
Compiling array bound check
  Consider the following C code
    int i, N;
    if ((i < N) && (i >= 0)) a[i]++;
    else go to EXIT
  Suppose i is in $1, N is in $2, a is an integer array and its starting address is in $3, and a[i] is allocated in $13
    sltu $4, $1, $2
    beq $4, $0, EXIT
    sll $4, $1, 2
    add $4, $4, $3
    lw $13, 0($4)
    addi $13, $13, 1

## Slide 81: Conditional branch instructions
Compiling complex conditions
  Suppose x, y, z are allocated to registers $11, $12, $13 and their addresses are in $1, $2, $3
    int x, y, z;
    if ((x == y) && (x >= 0)) z++;
    else z--;
    MIPS assembly language program:
    lw $11, 0($1)
    lw $12, 0($2)
    lw $13, 0($3)
    bne $11, $12, Label1
    bltz $11, Label1
    addi $13, $13, 1
    j Label2
    Label1: addi $13, $13, -1
    Label2: sw $13, 0($3)
Short circuit

## Slide 82: Conditional branch instructions
Compiling complex conditions
  Suppose x, y, z are allocated to registers $11, $12, $13 and their addresses are in $1, $2, $3
    int x, y, z;
    if ((x == y) || (x >= 0)) z++;
    else z--;
    MIPS assembly language program:
    lw $11, 0($1)
    lw $12, 0($2)
    lw $13, 0($3)
    beq $11, $12, Label1
    bgez $11, Label1
    addi $13, $13, -1
    j Label2
    Label1: addi $13, $13, 1
    Label2: sw $13, 0($3)
Short circuit
Fall through and jump paths
can be identified only after
the C code is compiled

## Slide 83: Conditional branch instructions
Compiling complex conditions
  Each clause is compiled from left to right
  If conjunction of clauses is used, the compiled code looks for the first false clause so that no further evaluation of clauses is necessary
  If disjunction of clauses is used, the compiled code looks for the first true clause so that no further evaluation of clauses is necessary
    Converts the if block into the jump path
    Fall through and jump paths cannot be correctly identified until the C code is compiled
  This compilation procedure is known as short-circuiting and saves time on average

## Slide 84: Conditional branch instructions
Compiling loops
  Consider the following while loop where a is an integer array (each element is four bytes)
    while (a[i] == k) i++;
  Assume that the starting address of array a is in $1, i is allocated to $2, k is allocated to $3, a[i] is allocated to $11, and address of i is in $12
    START: sll $4, $2, 2
    add $4, $4, $1
    lw $11, 0($4)
    bne $11, $3, EXIT
    addi $2, $2, 1
    j START
    EXIT: sw $2, 0($12)

## Slide 85: Conditional branch instructions
Compiling loops
  Consider the following while loop where a is an integer array (each element is four bytes)
    while (a[i] == k) i++;
  Assume that the starting address of array a is in $1, i is allocated to $2, k is allocated to $3, a[i] is allocated to $11, and address of i is in $12
    Optimized translation (why is it better than the previous?):
    sll $4, $2, 2
    add $4, $1, $4
    START: lw $11, 0($4)
    bne $11, $3, EXIT
    addi $2, $2, 1
    addi $4, $4, 4
    j START
    EXIT: sw $2, 0($12)

## Slide 86: Conditional branch instructions
Compiling “for” loops
  Consider the following “for” loop where a is an integer array (each element is four bytes)
    for (i=0; i<N; i++) a[i]++;
  Suppose i is in $1, N is in $2, the starting address of array a is in $3, and a[i] is allocated in $13
    xor $1, $1, $1
    blez $2, EXIT
    START: lw $13, 0($3)
    addi $13, $13, 1
    sw $13, 0($3)
    addi $3, $3, 4
    addi $1, $1, 1
    slt $4, $1, $2
    bne $4, $0, START
    EXIT: …

## Slide 87: Conditional branch instructions
Conditional branches do not have any destination operand
  At most two source operands for comparison
    Two source register operands in beq and bne
    One source register operand in blez, bltz, bgez, bgtz
  Branch target is a constant and is represented as an immediate operand
    Branch target or the label used in a branch instruction is the memory address where the target instruction is stored
    Compiler usually does not know instruction addresses because these get fixed at a later stage
    The branch target in a conditional branch instruction is encoded as how many instructions away the target is from the branch instruction (often called “offset”)

## Slide 88: Conditional branch instructions
Representing targets in conditional branches
  Consider the following translation of a “for” loop
    xor $1, $1, $1
    blez $2, EXIT // EXIT is encoded as 7
    START: lw $13, 0($3)
    addi $13, $13, 1
    addi $3, $3, 4
    addi $1, $1, 1
    slt $4, $1, $2
    bne $4, $0, START // START is encoded as -5
    EXIT: …
  A conditional branch with a positive offset is known as a forward branch; otherwise it is called a backward branch
Forward branch
Backward branch

## Slide 89: Conditional branch instructions
Representing targets in conditional branches
    xor $1, $1, $1
    blez $2, EXIT // EXIT is encoded as 7
    START: lw $13, 0($3)
    addi $13, $13, 1
    addi $3, $3, 4
    addi $1, $1, 1
    slt $4, $1, $2
    bne $4, $0, START // START is encoded as -5
    EXIT: …
  Target for a conditional branch instruction is computed by adding the offset multiplied by instruction size to the branch instruction’s address
    Works only if all instructions have the same size
    All MIPS instructions have the same size (four bytes)
Address A
Address A+4
Address A+28
Target = A+4+4*7
Target =
A+28+4*(-5)

## Slide 90: Compiling switch/case
The successful case is not fixed
    for (i=0; i<N; i++) {
    switch (x[i]) {
    case 0: …
    case 1: …
    …
    default: …
    }
    }
One possibility is to treat the chain of cases as if-else if-else chain
  The number of comparisons depends on the position of the successful case in the chain
  There can be a lot of wasted comparisons

## Slide 91: Compiling switch/case
A better option is to prepare a table where each entry is a case label and index into the table is the case value
  In the last slide’s example, let’s refer to this table by the array T (usually known as jump table)
    T[x[i]] should store the target case label
    Compiler is responsible for populating this table with the correct case labels
  Explains why only integer or character type is allowed in switch argument
  The compiler must generate an instruction to jump to the correct label
    This is an unconditional jump with a variable target
    The j instruction is allowed to use a constant target

## Slide 92: Compiling switch/case
The code will be transformed by the compiler
      for (i=0; i<N; i++) {
      switch (x[i]) {
      label0: case 0: …
      label1: case 1: …
      …
      labelD: default: …
      }
      }
    Transformed code:
      for (k=0; k<JTSize; k++) T[k] = labelD
      T[0] = label0; T[1] = label1; …
      for (i=0; i<N; i++) goto T[x[i]];
The compiler must generate an instruction to jump to the correct label (for goto T[x[i]])
    This is an unconditional jump with a variable target
    The j instruction is allowed to use a constant target

## Slide 93: Compiling switch/case
MIPS ISA provides an instruction to make unconditional jumps to variable targets
  This instruction is jr (jump register)
    Has one register operand holding the jump target
    Compiler is responsible to generate code for loading the correct target in the register before the jr instruction
    jr $20
    Takes the contents of $20 and treats it as a jump target
      This target is NOT an offset relative to the address where the jr instruction is stored
      This target is the absolute final target

## Slide 94: Compiling switch/case
Consider the following C code
    switch (x[i]) {
    case 0: …
    case 1: …
    …
    default: …
    }
    Suppose jump table starting address is in $1, starting address of x is in $2, i is in $3, x is an integer array, and x[i] is allocated in $12
      sll $4, $3, 2
      add $4, $4, $2
      lw $12, 0($4)
      sll $12, $12, 2
      add $4, $12, $1
      lw $4, 0($4) // Each jump table entry is 32 bits
      jr $4

## Slide 95: Compiling switch/case
MIPS translation shown in the last slide is not particularly efficient
  This translation works if we know the range of values x[i] can take
  Wastes a lot of memory by preparing a jump table for the entire range of x[i]
  Jump table size can be optimized by doing a simple range check on x[i] before using the jump table entry indexed by x[i]
    All values of x[i] outside the range of case labels can be mapped to one jump table entry representing the default target

## Slide 96: Compiling switch/case
If case labels are not consecutive, a lot of jump table space is wasted
  A simple range check on x[i] is not enough
Compiling switch/case is fundamentally a search problem in general
  Need to search for x[i] in the jump table and pick the corresponding case target
  Any efficient search technique can be used
    Hash tables are particularly attractive due to low average search time

## Slide 97: Procedure/Function call
Calling and returning from a function involves six steps
  Caller puts the function parameters at appropriate places so that the function (sometimes referred to as callee) can access them
  Jump to the first instruction of the function
  Acquire portions of memory required for executing the function
  Execute the instructions of the function
  Put return values at appropriate places so that the caller can access them after return
  Jump back to the origin of call

## Slide 98: Procedure/Function call
Where to put the function arguments?
  MIPS function calling convention recognizes that the registers are the fastest storage options
  It specifies four registers for passing function arguments
    Usually denoted by $a0, $a1, $a2, $a3
    Same as $4, $5, $6, $7
  If a function has more than four arguments
    First four are passed in registers
    Rest of the arguments are spilled to memory and the function will have to fill them in registers before it can operate on them
      Recall that the arithmetic and logic instructions in MIPS allow only register or immediate operands

## Slide 99: Procedure/Function call
How to jump to the function?
  This is an unconditional jump with a constant jump target
  Jumping to the function requires an additional operation
    Remembering where to come back and start execution after the function completes
  MIPS ISA offers an instruction called jump and link (jal) to carry out both operations
    jal target
    Target is usually the address of the first instruction of the function
    Jumps to target and saves the address of the next instruction in $ra (stands for return address and same as $31)

## Slide 100: Procedure/Function call
Instruction addresses have a special name
  Called program counter (PC)
  Every instruction has a unique PC
  If an instruction K has the PC equal to x, the next instruction would have PC x+s where s is the size of the instruction K in bytes
  In MIPS, s=4 for all instructions
    PC increases in steps of four
Suppose the PC of a jal instruction is x
  The PC of the instruction where the function should return to is x+4
  The jal instruction will store x+4 in $31

## Slide 101: Procedure/Function call
How to jump to a function?
  Assume that the PC of the first instruction of the function is y
  The generated instruction for jumping to the function is “jal y”
    The target is not exactly y, but for now we will assume that
    Assume that the PC of the jal instruction is x
    Stores x+4 in $31
  The same function can be called from different places in the program
    Each call will be translated to a corresponding jal instruction
    Each jal instruction will store a different return address in $31

## Slide 102: Procedure/Function call
How to jump to a function?
      a: f()  jal x ($ra is filled with a+4)
      …
      b: f()  jal x ($ra is filled with b+4)
      …
      …
      c: f()  jal x ($ra is filled with c+4)
      x: f() {
      …
      …
      }
  The jal instruction not only jumps to the function, but also establishes a link between the function and the caller by saving the return address

## Slide 103: Procedure/Function call
Where to put the return value of the function?
  This needs to be fixed so that the caller can access and use the return value
  Before the function returns, the return values are stored in $v0 and $v1 (same as $2 and $3)
  Usually, $v0 would be used only since only one value can be returned from a function
  In 32-bit MIPS, if a function returns a 64-bit value, the return value is split into two 32-bit values and placed in $v0 and $v1
    The caller can figure out whether both registers contain the return value or only $v0 contains the return value by looking at the type of the return value
    $v0 contains the most significant word for 64-bit value

## Slide 104: Procedure/Function call
How to jump back to the origin of the call?
  Recall that the jal instruction before jumping to the function saved the return address in $31
  Jumping back to the call site is accomplished with a single instruction: jr $31
    This instruction ends the function
  Inside the processor, a register stores the next instruction’s program counter
    The content of this register is used to fetch the next instruction from memory
  The “jr $31” instruction copies the contents of $31 into the program counter register
  In general, all branch and jump instructions copy the target into the program counter register

## Slide 105: Procedure/Function call
How to acquire and release memory required by a function?
  A function receives its first four parameters in four registers
  The remaining parameters are spilled into memory
  Additionally, the function may require some memory space for spilling registers
    Happens when the compiler runs out of registers while compiling the function
    In such situations, it must free up some registers, but it cannot just overwrite these registers
    These registers are first saved in memory and later before returning, these registers are restored by copying them back from memory (caller may need the old values)

## Slide 106: Procedure/Function call
How to acquire and release memory required by a function?
  The memory region usable by a function for spilling registers or function parameters belongs to a larger memory region known as the stack
  After compiling a function, the compiler estimates how much stack area the function will require
    This much stack area is reserved for the function
  Spilling on to the stack is called pushing on the stack
    Requires adjusting the top of stack pointer (or simply stack pointer) so that the next push doesn’t overwrite the value at the top of stack
    The stack pointer is maintained in $sp (same as $29)

## Slide 107: Procedure/Function call
How to acquire and release memory required by a function?
  The stack grows downward meaning from higher address toward lower address
    Pushing a 32-bit register requires decreasing $sp by four so that $sp now holds the address of the top of the stack
    Initially, $sp holds the address of the bottom of the stack
s bytes
BoS (address x)
ToS (address x-s)
$sp =
x - s

## Slide 108: Procedure/Function call
How to acquire and release memory required by a function?
  No special instruction for pushing on to the stack
    Spilling to stack is accomplished through a store instruction to 0($sp)
      sw $4, -4($sp) // Spills $4 to stack
      addi $sp, $sp, -4 // Adjusts $sp
      sb $5, -1($sp) // Spills only the least significant byte of $5
      addi $sp, $sp, -1 // Adjusts $sp
    Filling from stack is accomplished through load instructions
      lb $5, 0($sp) // Restores $5
      lw $4, 1($sp) // Restores $4
  Freeing a portion of the stack is accomplished by increasing $sp by an appropriate amount
    Known as popping the stack

## Slide 109: Procedure/Function call
How to acquire and release memory required by a function?
  The stack region allocated to a function is popped at the end of the function
      addi $sp, $sp, positive_constant // compiler knows the value
    This restores $sp to the point where it was before the function is called
    This is important for the caller function to work correctly after the callee function returns
      In C programming language, a function can be called only by a function, except for the main function which is called by a startup code that is attached with every program during linking

## Slide 110: Procedure/Function call
Example
      int example (int g, int h, int i, int j) {
      return ((g+h) – (i+j));
      }
      int main (void) {
      int x = example (12, 1, 34, 42);
      return 0;
      }
    MIPS translation
      example: add $a0, $a0, $a1 // g+h
      add $v0, $a2, $a3 // i+j
      sub $v0, $a0, $v0
      jr $ra
      main: addi $sp, $sp, -4 // creates space for 32 bits on stack (used later)
      addi $a0, $0, 12
      addi $a1, $0, 1
      addi $a2, $0, 34
      addi $a3, $0, 42
      sw $ra, 0($sp) // Use the created stack space for saving $ra
      jal example // This instruction overwrites $ra
      add $v0, $0, $0
      lw $ra, 0($sp)
      addi $sp, $sp, 4
      jr $ra

## Slide 111: Procedure/Function call
Example
  In this example, the “example” function does not require any stack space and the “main” function requires just four bytes on stack to save $ra before calling “example”
  More complex functions may require more space on the stack if they use a lot of variables
    For example, if the “example” function has five parameters and if the fifth parameter is an integer, the main function would reserve eight bytes on stack for it
      Four bytes would be used to save $ra before calling “example”
      Four bytes would be used to store the fifth parameter of “example”

## Slide 112: Procedure/Function call
Example (assume that “example” has five parameters all of integer type)
    MIPS translation
      main: addi $sp, $sp, -8 // Just one instruction to adjust $sp
      addi $a0, $0, 12
      addi $a1, $0, 1
      addi $a2, $0, 34
      addi $a3, $0, 42
      addi $v0, $0, 9 // Fifth parameter value is 9
      sw $ra, 4($sp)
      sw $v0, 0($sp)
      jal example
      add $v0, $0, $0
      lw $ra, 4($sp)
      addi $sp, $sp, 8
      jr $ra
      example: lw $1, 0($sp)
      …

## Slide 113: Procedure/Function call
MIPS register saving convention
  A function can use $8 to $25 for allocating variables
    $8 to $15 and $24 and $25 are referred to as temporary registers ($t0 to $t7 and $t8 and $t9)
    $16 to $23 are referred to as saved registers ($s0 to $s7) meaning that the function is supposed to save the contents of these registers on stack before using them and restore them after using them
      Also referred to as callee saved registers
      $sp and $ra are also callee saved registers
      The contents of callee saved registers are preserved across calls because the called function saves and restores them
    $t0 to $t9 are not preserved across calls
      Caller must save them on stack before calling a function if the caller wants the contents of any of these to be preserved
      Referred to as caller saved registers

## Slide 114: Procedure/Function call
MIPS register saving convention clearly specifies which registers are saved by the caller and which are saved by the callee
  Helps minimize the number of spills and fills
  If the caller wants the contents of any of the caller saved registers to be preserved, it must spill them to stack before calling a function
    $t0 to $t9, $a0 to $a3, $v0, $v1
    The callee does not worry about saving any of these registers; it can directly use them
  If the callee wants to use any of the callee saved registers, it must save them to stack before using them and restore them from stack after using them
    $s0 to $s7, $sp, $ra
    The caller does not worry about saving any of these before calling a function

## Slide 115: Procedure/Function call
MIPS register saving convention clearly specifies which registers are saved by the caller and which are saved by the callee
  A function first uses $t0 to $t9, $a0 to $a3, $v0, $v1 for allocating its variables before trying to use $s0 to $s7
    Using $s0 to $s7 requires spilling them to stack and restoring them back
    To minimize spills, it is always better to first exhaust the caller saved register set i.e., $t0 to $t9, $a0 to $a3, $v0, $v1

## Slide 116: Procedure/Function call
Example: compiling recursive function
        int factorial (int n) {
        if (n < 1) return 1;
        else return n*factorial(n-1);
        }
    MIPS translation:
        factorial: slti $t0, $a0, 1
        beq $t0, $0, Label
        addi $v0, $0, 1
        jr $ra
        Label: addi $sp, $sp, -8
        sw $ra, 4($sp)
        sw $a0, 0($sp)
        addi $a0, $a0, -1
        jal factorial
        lw $a0, 0($sp)
        mult $v0, $a0, $v0 // Not a correct MIPS instruction
        lw $ra, 4($sp)
        addi $sp, $sp, 8
        jr $ra

## Slide 117: Procedure/Function call
Functions in C access two types of variables
  Automatic: local to function and discarded when the function returns
  Static: global variables and anything declared as static; persist across calls and returns
  All automatic variables are allocated on stack
    Accessed using appropriate offsets relative to $sp
    When a function returns, $sp is incremented so that all automatic variables of that function are popped
  All static variables are allocated to the static or global region of memory
    Accessed using appropriate offsets relative to $gp (same as $28)
    $gp is a callee saved register

## Slide 118: Procedure/Function call
Stack portion created for a function’s automatic variables is called a procedure frame or activation record
  MIPS ISA defines a register known as frame pointer ($fp or $30) which can be used to record the bottom of the procedure frame
    $sp points to the top of the stack
Caller
Caller
Callee
Caller
High addr
High addr
High addr
Low addr
Low addr
Low addr
Before jal
During function
After return
$fp
$fp
$fp
$sp
$sp
$sp

## Slide 119: Procedure/Function call
Why frame pointer is needed?
  All automatic variables can already be accessed using displacements relative to $sp
  $fp offers another alternative where all automatic variables can be accessed using displacements relative to $fp
    Advantage is that $fp does not change during the function, but $sp can be adjusted from time to time during the function to push or pop variables
    Assembly language functions written using $sp can be hard to understand due to the changing values in $sp
      The same variable pushed on the stack at the beginning of a function can be referred to as d($sp) at one point in the function and as d’($sp) at another point in the function
      This variable referred to relative to $fp will have the same displacement throughout the function because $fp always points to the bottom of the procedure frame

## Slide 120: Procedure/Function call
Structure of procedure stack frame
  Before $sp is decremented by frame size, $fp is saved at -4($sp) and then $fp is set to $sp-4
Saved $fp
Spilled arguments (if any)
Callee saved registers (if any)
Local arrays and structures
$fp
$sp
Decreasing address

## Slide 121: Procedure/Function call
Frame pointer is not used by some compilers
  MIPS C compiler does not use $fp for pointing to the bottom of the procedure frame
    Sacrifices readability of code
  Instead, $fp is used as a regular callee saved register to expand the set of registers that can be used for allocating variables
    Reduces number of spills to improve performance

## Slide 122: Procedure/Function call
So far we have assumed that a function call has a constant target known to the compiler
  These are known as direct calls
C programming language allows function pointers
  A function pointer can point to any legitimate function
  The value of a function pointer is the PC of the first instruction of the function it points to
  During the execution of a program, a function pointer can be assigned different values
    Just like any other pointer variable

## Slide 123: Procedure/Function call
Example use of function pointer
      int f (int x, int y) {
      return x+y;
      }
      int g (int x, int y) {
      return x-y;
      }
      int main (void) {
      int (*fptr)(int, int);
      int a, b, c;
      scanf(“%d %d”, &a, &b);
      if (a > b) fptr = g;
      else fptr = f;
      c = fptr(a, b);
      printf(“%d\n”, c);
      return 0;
      }
Target unknown at compile time

## Slide 124: Procedure/Function call
Calls made using function pointers are known as indirect calls
Compiling indirect calls requires something like jr instruction with the linking facility so that the return address can be saved
MIPS ISA offers the jump and link register (jalr) instruction for compiling indirect calls
  Takes a register operand and uses the content of the register as the call target: jalr $20

## Slide 125: Procedure/Function call
Translating indirect calls
  Consider the following code snippet
      if (a > b) fptr = g;
      else fptr = f;
      c = fptr(a, b);
    Suppose f starts at PC x and g starts at PC y (these constants are known at compile time)
    Suppose fptr is in $11, a is in $12, and b is in $13
    MIPS translation
      slt $t0, $13, $12
      beq $t0, $0, label
      la $11, y # pseudo-instruction (load label address)
      j label1
      label: la $11, x # pseudo-instruction (load label address)
      label1: add $a0, $0, $12
      add $a1, $0, $13
      addi $sp, $sp, -4
      sw $ra, 0($sp)
      jalr $11
      …

## Slide 126: Procedure/Function call
Data allocated dynamically within a function resides in a portion of memory known as the heap
  Any pointer to heap data would still be allocated in registers if the pointer is local to the function
    Local pointers are treated as automatic variables and can be spilled to stack if the compiler is short of registers
    Local pointers cannot be used outside the function because the registers allocated to them may get overwritten by the caller after the function returns

## Slide 127: 32-bit MIPS memory map
A program’s memory has four regions: code (also called text), static/global data, heap data, stack data
  Code region stores the instructions of the program and starts at address 0x004000000
  Above code region is the static/global region starting at address 0x10000000
    All data in this region are accessed relative to $gp which is initialized to the mid-point (address 0x10008000) of the static/global region
    The displacement used with $gp can be positive or negative such that any data from address 0x10000000 to 0x1000ffff can be accessed

## Slide 128: 32-bit MIPS memory map
Stack
Heap
Static/Global
Code/Text
Reserved
Addresses
0
0x004000000
0x10000000
0x10010000
Initial $sp = 0x7ffffffc
Reserved
$gp = 0x10008000

## Slide 129: Instruction encoding
A program is compiled into a sequence of instructions and is stored in a binary file
  Requires each instruction to be encoded in binary (machine language)
Before a program can start running at least part of this binary needs to be loaded in DRAM from the binary file
  The file usually resides in a non-volatile storage medium such as the hard disk
  The remaining parts can be loaded in DRAM as and when needed
How to encode instructions in binary?

## Slide 130: Instruction encoding
Each part of an instruction must be encoded in binary
  The instruction opcode and the operands
  The operands can be addressing registers or memory location or can be constants
  MIPS ISA allows only loads and stores to have memory operands
    Requires encoding a signed displacement in addition to the base register
  MIPS ISA allows at most one operand to be a constant or immediate
    Is it useful to have more than one immediate operand?

## Slide 131: Instruction encoding
Each part of an instruction is referred to as a field
  Fields to encode two source register addresses and a destination register address are required
    Each of these is five bits wide because MIPS ISA has 32 registers
  Width of the opcode field depends on the number of different types of instructions
    MIPS ISA dedicates six bits to the opcode field: 64 different instructions
    Additionally, there is a six-bit wide function field that is used to encode subtypes of instructions with opcode zero
      Opcode zero is used for a subset of arithmetic and logic instructions that have no immediate operands

## Slide 132: Instruction encoding
Arithmetic and logic instructions execute in the arithmetic-logic unit (ALU)
  A subset of instructions that have opcode zero (the function value is shown in parentheses)
    sll (0x0), srl (0x2), sra (0x3), sllv (0x4), srlv (0x6), srav (0x7), jr (0x8), jalr (0x9), mfhi (0x10), mthi (0x11), mflo (0x12), mtlo (0x13), mult (0x18), multu (0x19), div (0x1a), divu(0x1b), add (0x20), addu (0x21), sub (0x22), subu (0x23), and (0x24), xor (0x26), nor (0x27), or (0x25), slt (0x2a), sltu (0x2b)
    These are ALU instructions that do not have any immediate operands
    Difference between add and addu instructions: addu instruction does not catch any overflow, but add does
      Nothing to do with whether the operands are signed or unsigned (same is true for sub and subu)

## Slide 133: Instruction encoding
Arithmetic and logic instructions execute in the arithmetic-logic unit (ALU)
  Multiplications are done through mult and multu instructions
    Difference between mult and multu is that multu treats operands as unsigned; none detects overflow
    These instructions do not have any explicit destination register and accepts only two source register operands
    Two special registers called Hi and Lo store the most significant and the least significant words of the 64-bit result in 32-bit MIPS
      mult $10, $20 // Multiplies $10 by $20 and sends the result to
      // Hi and Lo registers

## Slide 134: Instruction encoding
Arithmetic and logic instructions execute in the arithmetic-logic unit (ALU)
  Integer divisions are done through div and divu instructions
    Difference between div and divu is that divu treats the operands as unsigned; no overflow in division
    These instructions do not have any explicit destination register and accepts only two source register operands
    Two special registers called Hi and Lo store remainder and quotient respectively
      div $10, $20 // Divides $10 by $20 and stores remainder in Hi
      // quotient in Lo
  Floating-point multiplication and division have separate instructions

## Slide 135: Instruction encoding
Arithmetic and logic instructions execute in the arithmetic-logic unit (ALU)
  The Hi and Lo registers cannot be used as operands of any ALU instructions
  To further process the results of multiplication and division, the Hi and Lo register contents must be moved to general purpose registers
  MIPS ISA offers two instructions to achieve this
    mfhi moves the contents of Hi to a specified register
      mfhi $t0
    mflo moves the contents of Lo to a specified register
      mflo $t6
  There are matching instructions to move to Hi and Lo also: mthi $X and mtlo $Y (rarely used)

## Slide 136: Instruction encoding
C language disables overflow detection
  MIPS C compiler always generates addu, subu
    Results are same as add, sub except that nothing additional happens on overflow
For multiplication involving signed operand types, mult is generated; otherwise multu is generated
For division involving signed operand types, div is generated; otherwise divu is generated
If overflow needs to be detected for mult and multu, it must be done in software
  MIPS doesn’t have any hardware support for detecting multiplication overflow

## Slide 137: Instruction encoding
Other than opcode and function fields, three fields are needed for specifying two source and one destination register operands
  These three fields can be five bits each because MIPS has 32 registers
To encode constant shift amounts (at most 31), we need a five-bit field
All instructions conforming to this format are called R-format instructions (opcode is zero)
  rs and rt are source register operands and rd is the destination register operand
opcode (6)
rs (5)
rt (5)
rd (5)
sh amt (5)
function (6)

## Slide 138: Instruction encoding
Not all fields are used by all instructions
  Non-shift instructions and variable shift instructions do not use sh amt
  sll, srl, and sra do not use rs
  jr does not use rt, rd
  jalr does not use rt (rd is always set to 31)
  mfhi and mflo do not use rs, rt
  mthi and mtlo do not use rt, rd
  mult, multu, div, divu do not use rd
  Unused fields are encoded as zero
Length of these instructions could be shortened, but MIPS designers wanted all instructions to have a fixed four-byte size
  Simple design, even though wastes memory

## Slide 139: Instruction encoding
R-format instructions have only register operands
Instructions having one immediate operand are encoded using the I-format
  Observation: these instructions require at most two register operands
  Both register operands could be source operands: beq, bne, all store instructions
  One register operand could be source and the other could be destination: addi, addiu, andi, ori, slti, sltiu, xori, all load instructions, lui
  Some I-format instructions use only one register operand as a source: blez, bgtz, bltz, bgez

## Slide 140: Instruction encoding
The immediate operand is treated differently for different types of I-format instructions
  Arithmetic instructions: signed immediate operand (addi, addiu, slti) or unsigned immediate operand (sltiu)
  Logical instructions: unsigned immediate operand (andi, ori, xori, lui)
  Branch instructions: PC-relative signed jump offset (beq, bne, blez, bltz, bgtz, bgez)
  Load and store instructions: signed displacement from the base register
opcode (6)
rs (5)
rt (5)
immediate (16)

## Slide 141: Instruction encoding
I-format instructions having one destination register operand use rt as the destination
I-format instructions having only one source register operand use rs as the source
The immediate operand is sign-extended to 32 bits for addi, addiu, slti, sltiu (treats the sign-extended value as unsigned), all branches, all loads and stores
The immediate operand is zero-extended to 32 bits for all logical instructions
opcode (6)
rs (5)
rt (5)
immediate (16)

## Slide 142: Instruction encoding
How to load a constant bigger than 16 bits into a register?
  Suppose we would like to load the value 0x123456 into $10
  Make use of the lui instruction (load upper immediate)
    lui $10, 0x12
    ori $10, $10, 0x3456

## Slide 143: Instruction encoding
Another use of lui: synthesizing addresses
  Suppose the compiler wants to generate instructions to load the word starting at address 0x789abc into register $10
    lui $1, 0x78 // $1 is also referred to as $at
    ori $1, $1, 0x9abc // $at is a register used by assembler
    lw $10, 0($1)
  Note that the last two instructions cannot be replaced by lw $10, 0x9abc($1)
  If the address was 0x345678, the following would work
    lui $1, 0x34
    lw $10, 0x5678($1)

## Slide 144: Instruction encoding
J-format is used to encode j and jal
A 32-bit target is created as follows
  The jump_target is shifted left by two bits to make it a four-byte aligned address
  The most significant four bits of the PC of the jump instruction are concatenated in front of the shifted jump_target
For conditional branches (I-format), the offset is shifted left by two bits, sign-extended, and added to PC to compute the branch target
opcode (6)
jump_target (26)

## Slide 145: Instruction encoding
16-bit branch offset in conditional branches also limits the distance to the branch target
  If the branch target is too far away from the branch instruction, an unconditional jump can be used along with the conditional branch
    if (x == y) { … } // Problem: very large if block
    else { … }
  MIPS translation (incorrect)
    bne $t0, $t1, else_label
    …
    j label
    else_label: …
    label: …
≥ 215 instructions

## Slide 146: Instruction encoding
16-bit branch offset in conditional branches also limits the distance to the branch target
  If the branch target is too far away from the branch instruction, an unconditional jump can be used along with the conditional branch
    if (x == y) { … } // Problem: very large if block
    else { … }
  MIPS translation (correct)
    beq $t0, $t1, if_label
    j else_label
    if_label: …
    j label
    else_label: …
    label: …

## Slide 147: Instruction encoding: Summary
All instructions are 32-bit long
Three formats distinguished by opcode
  R-format: opcode is zero [op:rs:rt:rd:shamt:func]
    Only register operands and shift amount
    Also known as ALU format or special format
    A very special R-format instruction: all zero (sll $0, $0, 0), known as NOP (no operation)
  J-format: opcode is j (2) or jal (3) [op:target]
  I-format: all other opcodes [op:rs:rt:immediate]
    Instructions with immediate operand
    Immediate is sign-extended in all instructions except logic instructions and lui
Unused fields in an instruction are set to zero

## Slide 148: Instruction encoding: Summary
Three formats taken together define five operand addressing mechanisms in MIPS ISA
  Immediate addressing mode
    Refers to constant operands
  Register addressing mode
    Refers to register operands
  Base/Displacement addressing mode
    Refers to memory operands
  PC-relative addressing mode
    Refers to the address of the conditional branch target
  Pseudo-direct addressing mode
    Refers to the address of the unconditional jump target and direct function call target

## Slide 149: Manipulating strings
C compiler stores a string as an array of characters
  Each character is a byte and is stored as its ASCII value
  The last character of a string is ‘\0’ which has ASCII value zero
  C programs involving string manipulation use lb, lbu, and sb instructions to move characters between registers and memory
Java compiler stores a character using 16-bit Unicode values
  Java programs involving string manipulation use lh, lhu, and sh instructions to move characters between registers and memory

## Slide 150: Floating-point instructions
MIPS ISA offers a separate set of floating-point instructions
  Manipulates floating-point data
  Floating-point registers are separate and there are 32 of them denoted $f0 to $f31, each 32 bits long in 32-bit MIPS
    Double precision values are stored using a pair of registers e.g., the double precision value in $f_2n refers to the pair $f_2n and $f_{2n+1}
      $f_2n contains the least significant word
    There is no floating-point register hardwired to zero
  All instructions are still 32 bits long
  IEEE 754 single-precision and double-precision

## Slide 151: Floating-point instructions
MIPS ISA offers a separate set of floating-point instructions
  Typical instructions are add, sub, mul, div, abs, mov, neg, compare, precision/type conversion, load, store, etc.
  Each instruction has two flavors: .s and .d
    add.s is a single-precision addition operation
      add.s $f0, $f1, $f2 // $f0  $f1 + $f2
    add.d is a double-precision addition operation
      add.d $f0, $f2, $f4 // {$f1, $f0}  {$f3, $f2} + {$f5, $f4}
  The mul and div instructions use explicit floating-point destination register as opposed to Hi/Lo
    mul.s $f0, $f1, $f2 // $f0  $f1*$f2
    div.s $f0, $f1, $f2 // $f0  $f1/$f2

## Slide 152: Floating-point instructions
MIPS ISA offers a separate set of floating-point instructions
  The mov instruction is needed due to absence of a hardwired zero register
    Moves from one floating-point register to another
      mov.s $f0, $f1 // $f0  $f1
      mov.d $f0, $f2 // {$f1, $f0}  {$f3, $f2}
  There are instructions to move between floating-point registers and general-purpose registers
    mfc1 and mtc1 instructions
    mfc1 $2, $f0 // $2  $f0
    mtc1 $3, $f0 // $f0  $3 (note the assembler syntax)
    Needed to manipulate the bits of a floating-point number
    Instructions having a mix of FPR and GPR operands

## Slide 153: Floating-point instructions
MIPS ISA offers a separate set of floating-point instructions
  The precision/type conversion instructions can convert between various types
    float to double
    double to float
    float to int
    double to long (or long long)
    Needed for different kinds of typecast operations
  All floating-point instructions have a single encoding [opcode:format:ft:fs:fd:function]
    add, sub, mul, div, abs, neg, mov, compare, type/precision conversion instructions have a common opcode (0x11) and gets distinguished by different function codes

## Slide 154: Floating-point instructions
MIPS ISA offers a separate set of floating-point instructions
  Floating-point instructions do not allow immediate operands
  Load and store instructions need to encode displacement
    lwc1 $f0, 20($10) // $f0  [$10 + 20] ($f0 is ft)
    swc1 $f0, 20($10) // [$10 + 20]  $f0 ($f0 is ft)
    Loading or storing a double-precision value generates two lwc1 or two swc1 instructions in 32-bit MIPS
    lwc1 and swc1 instructions use the I-format of integer instructions where rt field specifies ft
opcode (6)
ft (5)
fs (5)
fd (5)
format (5)
function (6)

## Slide 155: Floating-point instructions
Floating-point instructions do not allow immediate operands in MIPS ISA
    This complicates translation of floating-point operations involving constants e.g., x = y + 1.5
    One option is to prepare the IEEE 754 representation of the constant in a general-purpose register and then move it to a floating-point register using mtc1
      Requires at least three instructions: lui, ori, mtc1
      Need to deal with pair of registers for double-precision
        Requires six instructions
      Takes away general-purpose registers for compiling floating-point operations
    If a constant is used at many places, another option is to store it in memory and load it into a floating-point register when needed
      Requires just one lwc1 instruction to get the constant in a floating-point register (two lwc1 for double-precision)

## Slide 156: Translating and starting a program
Four-step process involving four different pieces of system software: compiler, assembler, linker, loader
  Compiler translates an HLL program into assembly language program
  An assembly language program specifies the program in terms of instructions and pseudo-instructions
    Pseudo-instructions are not supported by the ISA, but are presented as a convenience
      move $4, $5 // add $4, $0, $5
      blt $4, $5, label // slt $at, $4, $5; bne $at, $0, label
      bgt, ble, bge
      li $5, 0x123456 // lui $5, 0x12; ori $5, $5, 0x3456

## Slide 157: Translating and starting a program
Assembler translates an assembly language program into an object file
  Cannot use pseudo-instructions any more
  Object file contains the program text in binary (machine language program), program data, and information to place instructions in memory
  Assembler assigns values to all labels in the program by maintaining a symbol table

## Slide 158: Translating and starting a program
A UNIX object file has six segments
  Header: describes the sizes and positions of the other segments
  Text: machine language program
  Static data: persistent data that live throughout the life of the program
  Relocation information: identifies instructions and data that depend on absolute addresses when the program is loaded into memory
  Symbol table: labels whose values are not resolved yet (external references e.g., externs)
  Debug information: how to associate instructions with HLL program statements and make data structures readable in the binary

## Slide 159: Translating and starting a program
Linker’s job is to “stitch together” multiple object files to create one single executable binary
  Each HLL program file is compiled and assembled independently to produce an object file
    prog.c to prog.s to prog.o
    All labels are resolved local to an object file by the assembler
  Linker (also known as link editor) takes all the object files and edits the labels and addresses to make them globally consistent across all object files of the executable

## Slide 160: Translating and starting a program
Linker executes three steps
  Place code and data symbolically in memory
  Determine the data addresses and instruction labels
  Resolve all internal and external references
Linker uses the relocation information and the symbol table to resolve all labels and addresses
Linker’s output is an executable binary file
  Has the same format as an object file with no unresolved label or address

## Slide 161: Translating and starting a program
Loader loads portions of the executable file into memory on demand, stores the main function’s arguments on stack, initializes the registers and stack pointer, sets the PC to point to the first instruction of the “start-up routine”
  The start-up routine copies the main function’s arguments from stack to argument registers and executes “jal main”
  When main function returns back to the start-up routine, the program exits
    This is done through the “exit system call” which frees all memory allocated to the program

## Slide 162: Translating and starting a program
C programs often use library functions
  This requires linking the program’s object files with the library object file(s)
Static linking links all required library object files with the program’s object files
  The resulting executable file can be quite large in size wasting space
  After the executable is built, if a bug in a library gets fixed or an improved version of the library is released, the executable will continue to use the old library unless the linking procedure is repeated
  This disadvantages are addressed through dynamic linking

## Slide 163: Translating and starting a program
A dynamically linked library invokes the linker only when the program calls a function belonging to the library object file
  Linker is invoked while the program is running
  Initial version of the dynamic linker was used to be invoked by the loader just before the program ran and the loader would link the required libraries
    Still links all required libraries as opposed to only the library functions that are called
  Today’s dynamic linkers do lazy procedure linking where a library function is linked at the time it is called

## Slide 164: Translating and starting a program
Loads the value
Jumps here;
jr uses the dest
register of lw
Changes the value
to point to DLL routine

## Slide 165: Translating and starting a program
First call to a dynamically linked library function has a very high overhead
Subsequent calls have lower overhead, but still requires an extra indirect jump (jr)
Dynamic linking saves space at the expense of extra instruction execution compared to static linking